## Slide 2: Learning Intentions
To identify different types of wood and their properties

## Slide 3: Success Criteria
I can state a type of softwood/hardwood/manufactured board
I can describe the properties of a type of wood
I can name different woods based on appearance
I can describe how a manufactured board is constructed

## Slide 4: Why do we need to know about types of wood?
Hardwoods and softwoods have different properties, this means that they can be used in different ways and for different products.

## Slide 5: How do I know the difference?
Most softwood trees have spiky leaves and are coniferous (Larch is an exception it’s deciduous) with branches forming in whorls (rings) of two or more at the same level.
Larch Tree

## Slide 6: How do I know the difference?
Hardwood Trees have broad, flat leaves and are deciduous (Yew and Holly being exceptions).
Branches usually grow at different levels and never more than two at the same level. Unlike softwoods which are specifically grown and forested most hardwoods, especially tropical ones, occur at random and are naturally growing.

## Slide 7
This makes felling and collection difficult raising the prices considerably against softwood. This fact, and of course diminishing stocks, have led to greater interest in lesser known hardwoods such as Utile
Utile Tree
In central Africa

## Slide 8
Meranti
Grown in the Philippines
Sometimes known as the Philippine’s Mahogany

## Slide 9: How do I know the difference?
Manufactured boards are made up of the scraps of trees and are compacted together by manmade processes.
The wood does not stick together on its own and needs an adhesive to chemically attach them together.
Formaldehyde is the commonly used compound to do this, however this is not safe to be exposed to over a length of time.

## Slide 10: Softwoods
 | Type Of Wood | Appearance | Properties | Uses
Softwoods | RED PINE | Light colour with reddish grain and knots | Long straight trunk, strong inexpensive, fast growing | Building, joinery
 | WHITE PINE | Light colour with light brown grain and small dark brown knots | Long straight trunk, strong inexpensive, fast growing | Building, joinery
 | CEDAR | Knot free, straight grain | Light, strong, resists rot | Weather boarding

## Slide 11: Softwoods

## Slide 12: Hardwoods
Hardwoods | OAK | Golden brown | Strong, durable | Gates, posts, boats, furniture
 | WALNUT | Brown with a fine grain | Works well, high quality finish | Furniture veneers
 | BEECH | Flecks on a light pinkish wood | Doesn’t split, hard and can be laminated into curves | Toys, furniture
 | MERANTI | Reddy Brown colour with specks | Easy to cut, strong gives a good finish | Toys, storage
 | ASH | Brown colour with darker brown grain | Robust, hardwearing | Joinery, furniture

## Slide 13: Hardwoods
Oak
Meranti
Mahogany

## Slide 14: Manufactured Boards
BLOCKBOARD | Blocks glued between veneers | Flat, stable, won’t warp or split, supplied in large sheets | Furniture, table tops, drawing boards, can be laminated with thermo-setting plastic to make worktops
PLYWOOD | Layers of thin wood |  | 
MDF | Smooth surface, no grain |  | 
CHIPBOARD | Smooth surface |  | 
HARDBOARD | Coarse texture, smooth one side, textured other |  | 

## Slide 15: Manufactured Boards

## Slide 16: Your Task
Write down:
How many softwoods you know.
How many hardwoods you know.
How many manufactured boards you know.

## Slide 17: Your Task
What are the properties of Red Pine?
What are the properties of Oak?
What are the properties of Plywood?

## Slide 18
Your Task
Write down:
Products are made of softwoods
Products are made of hardwoods
Products are made of manufactured boards